## Slide 2: 實驗
3. Evaluate the ADC
將TRIGGER SELECT設定成Internal, RATE SELECT設定成20kHz, 調整VOLTAGE CONTROL讓ADC state位在0bits(面板bit)
緩慢增加input voltage並且觀察output的ADC變化。MSB是最左邊的bit，LSB是最右邊的bit。調整電壓直到LSB變成閃動。有可能沒辦法產生全亮或是全暗。
麵包板皆可變電阻 或是layout, 面板可以調整bit數 4.8.12，左移位元
LCD(i2c) / 可變電阻給電壓 / ADC1
LCD : ADC1 value input
Pinout : real voltage ouput
Set the TRIGGER SELECT to Internal and RATE SELECT to 20 kHz and adjust VOLTAGE CONTROL so that the ADC state is at zero bits (i.e. so that none of the LED lights are illuminated).
Slowly increase the input voltage and observe the voltage at which the output of the ADC changes. The most significant bit (MSB) is the left LED and the least significant bit (LSB) is the right LED. Adjust the voltage to the point at which the LED representing the LSB "twitches." Note that you may not be able to get all of the lights to go on or off at the extreme ends of the range.

## Slide 3: 實驗
4. Evaluate the Static Response of the D/A Converter
沒有負準位 , 0-3.3
量ADC 跟 DAC的誤差
DAC1
Adjust the input voltage as indicated below and observe the input. After the input voltage is set, push the trigger button. Then observe the output voltage by connecting the meter to the OUTPUT. The input and output can be measured by switching the OUTPUT SELECT between Input and Output. Note that the limiting voltages below may not be obtainable due to power supply drift.

## Slide 4: 實驗
5. Dynamic Response of System
3V p-p / 1.5V offset (截波電路) (GPIO 0-4 clock select / 5-7 bit select)
訊號產生器要接INPUT 1 (ADC1) / 然後還有接在示波器CH1 (DAC1)
Rate select 20kHz 接在示波器CH2 (clock source DMA) / 訊號產生器高於100 Hz
Set RATE SELECT to 20kHz, 10 kHz, 5 kHz, 1 kHz, and .5 kHz. Observe the OUTPUT at each setting.
將Rate select 1kHz, function generator to about 1100 Hz 緩滿增加(1Hz)
畫圖
Adjust the input voltage as indicated below and observe the input. After the input voltage is set, push the trigger button. Then observe the output voltage by connecting the meter to the OUTPUT. The input and output can be measured by switching the OUTPUT SELECT between Input and Output. Note that the limiting voltages below may not be obtainable due to power supply drift.

## Slide 5: 實驗
6. Filter Effects
用撥盤做濾波器 1k/ 5k/ 10k (software RC filter ) (GPIO 8-10)
Set the function generator frequency to 100 Hz.
Set RATE SELECT to 20 kHz and observe the OUTPUT with the FILTER SELECT set at the 10 kHz cutoff.
Repeat with the FILTER SELECT set at the 5 kHz cutoff.
Now change the function generator OUTPUT to a square wave at 1 kHz and observe the OUTPUT for the various combinations.

## Slide 6: 實驗
7. Small Amplitude Effects
Set the function generator back to a 1 kHz sine wave and adjust its amplitude to 0.05 Volts peak to peak (0.04 Volts RMS).
How well does the OUTPUT represent the INPUT under the best selection of sample rate and filter setting?
Reduce the input voltage further to about 0.02 Volts RMS.
What is the main problem?
Illustrate your results with a sketch.
問大郭

## Slide 7: 實驗
8. 放音樂
用Input2(3.5mm公頭)輸入音樂 改bit數 還有SAMPLE RATE 用output聽音樂
3.5mm公頭 接頭